8.1_1
“Parameters defining the conditions for requesting an MA”
source	8.1
users	8.2,
internal_T_CYCRQST		Time repeating the MA request, i.e. an MA shall be requested if the time elapsed since the last MA request reaches this value.
internal_T_MAR		Time, before reaching the indication point, at which an MA request shall be sent.
internal_T_TIMEOUTRQST		Time, before any MA-timer elapses, at which an MA request shall be sent

XXX
Level 2/3 transistion information
source	XXXXXXXXXXXXXX
users	8.2, “function to delete the information”
		Marker, indicating that a level 2/3 transition has been announced
		Marker, indicating that an MA has been requested (for the level 2/3 transition)
		Marker indicating that radio communication to the RBC responsible after the transition to level 2/3 has been established.

XXX

source	XXXXXXXXXXXXXX
users	8.2, “xxxxxx”
		Start of Mission status xxxxxxxxxx

8.2_1
MA request information
source	8.2
users	“output function building message 132”
		Marker indicating that an MA shall be requested
		Indicator defining the reason for requesting an MA (3.8.2.8, 7.5.1.118.3)

8.2_2
“MA request timer” (up counter), maximum value: XXXXXXX
	“Running time” (special value for “infinite”)
	“Status”: “started” or “not started”

8.3_1
MA structure: one variable
	The number of sections in the MA (default 0, maximum including the end section: 34)
	Sections as defined in 8.3_3
	End section information (additional information concerning the furthest MA section): / An “end section timer start location” (related to the LRBG) (default: infinite) / An “end section timer” / Limit of authority speed. (default: 0) / A Limit of authority “(LOA) timer / Danger point distance: distance beyond EOA to the danger point (“0” if not available) (default: 0) / The release speed related to the danger point. (default: 0) / Overlap distance: the distance beyond the EOA to the end of the overlap (default: 0) / The release speed related to the overlap. (default: 0) / The overlap timer start location (related to the LRBG) (default: infinite) / An “overlap timer”
	The signalling related maximum speed (only applicable in level 1)

8.3_2
General MA-timer (down counter)
	“Remaining time” (special value for “infinite”) (default: infinite)
	“Status”: “started” or “not started” (default: not started)
	“stop location” (related to the LRBG) (special value for “infinite”) (default: infinite)

8.3_3
An MA section
	The “starting location of the section” related to the LRBG.
	The “length of the section”
	The “sender of the MA”: level1 device or RBC identity
	A “section timer” (as defined in 8.3_2)